## Slide 1: kathara lab
basic IPv6 configuration, ping, traceroute and ICMPv6
Version | 1.0
Author(s) | L. Ariemma, T. Caiazzi, G. Di Battista
E-mail | contact@kathara.org
Web | http://www.kathara.org/
Description | basic IPv6 configuration commands, IPv6 stateless auto-configuration, usage of ping and traceroute, ICMPv6 behaviour

## Slide 2: copyright notice
All the pages/slides in this presentation, including but not limited to, images, photos, animations, videos, sounds, music, and text (hereby referred to as “material”) are protected by copyright.
This material, with the exception of some multimedia elements licensed by other organizations, is property of the authors and/or organizations appearing in the first slide.
This material, or its parts, can be reproduced and used for didactical purposes within universities and schools, provided that this happens for non-profit purposes.
Information contained in this material cannot be used within network design projects or other products of any kind.
Any other use is prohibited, unless explicitly authorized by the authors on the basis of an explicit agreement.
The authors assume no responsibility about this material and provide this material “as is”, with no implicit or explicit warranty about the correctness and completeness of its contents, which may be subject to changes.
This copyright notice must always be redistributed together with the material, or its portions.

## Slide 3: content of the lab
there are two routers, called r1 and r2, and three hosts, called pc1, pc2, and pc3
  they are connected via three LANs
  we force their MAC addresses to be easily readable
we will learn how to:
  administratively assign an IPv6 address and a netmask to the interface of a system
  administratively assign a default gateway to the interface of a system
  set the IPv6 addresses of a group of end-systems using the MAC-address-based stateless-auto configuration
  set the routing table of a router
we will use the ping and traceroute commands
we will observe the behavior of ICMPv6
© Computer Networks Research Group Roma Tre

## Slide 4: lab configuration

## Slide 5: network topology – high level view
r2
pc2
pc3
pc1
r1

## Slide 6: network topology – MAC addresses
A
r1
r2
C
B
pc1
pc2
eth0
eth0
eth0
eth1
eth1
eth0
pc3
eth0
0:1
0:2
0:3
0:a1
0:c1
0:b1
0:b2

## Slide 7: network topology – IPv6 address plan
A
r1
r2
C
B
pc1
pc2
eth0
eth0
eth0
eth1
eth1
eth0
2001:0:0:1::/64
2001:0:0:3::/64
2001:0:0:2::/64
.1
.1
.1
.2
pc3
eth0
0:1
0:2
0:3
0:a1
0:c1
0:b1
0:b2
Will be assigned using SLAAC (StateLess Address Auto-Configuration)

## Slide 8: a quick look at the lab
pc1[0]="A"
pc1[image]="kathara/base"
pc1[ipv6]="True"
pc1[sysctl]="net.ipv6.conf.eth0.accept_ra=2"
pc2[0]="C"
pc2[image]="kathara/base"
pc2[ipv6]="True"
pc2[sysctl]="net.ipv6.conf.eth0.accept_ra=2"
pc3[0]="C"
pc3[image]="kathara/base"
pc3[ipv6]="True"
pc3[sysctl]="net.ipv6.conf.eth0.accept_ra=2"
wireshark[bridged]=true
wireshark[port]="3000:3000"
wireshark[image]="lscr.io/linuxserver/wireshark"
wireshark[num_terms]=0
lab.conf
r1[0]="A"
r1[1]="B"
r1[image]="kathara/base"
r1[ipv6]=“True"
r2[0]="C"
r2[1]="B"
r2[image]="kathara/base"
r2[ipv6]=“True"
lab.conf

## Slide 9: a quick look at the lab
pc1[0]="A"
pc1[image]="kathara/base"
pc1[ipv6]="True"
pc1[sysctl]="net.ipv6.conf.eth0.accept_ra=2"
pc2[0]="C"
pc2[image]="kathara/base"
pc2[ipv6]="True"
pc2[sysctl]="net.ipv6.conf.eth0.accept_ra=2"
pc3[0]="C"
pc3[image]="kathara/base"
pc3[ipv6]="True"
pc3[sysctl]="net.ipv6.conf.eth0.accept_ra=2"
wireshark[bridged]=true
wireshark[port]="3000:3000"
wireshark[image]="lscr.io/linuxserver/wireshark"
wireshark[num_terms]=0
lab.conf
r1[0]="A"
r1[1]="B"
r1[image]="kathara/base"
r1[ipv6]=“True"
r2[0]="C"
r2[1]="B"
r2[image]="kathara/base"
r2[ipv6]=“True"
lab.conf
Accept router advertisements on eth0

## Slide 10: a quick look at the lab
ip link set dev eth0 address 00:00:00:00:00:01
ip link set dev eth0 down
ip link set dev eth0 up
pc1.startup
ip link set dev eth0 address 00:00:00:00:00:02
ip link set dev eth0 down
ip link set dev eth0 up
pc2.startup
ip link set dev eth0 address 00:00:00:00:00:03
ip link set dev eth0 down
ip link set dev eth0 up
pc3.startup

## Slide 11: a quick look at the lab
ip link set dev eth0 address 00:00:00:00:00:01
ip link set dev eth0 down
ip link set dev eth0 up
pc1.startup
ip link set dev eth0 address 00:00:00:00:00:02
ip link set dev eth0 down
ip link set dev eth0 up
pc2.startup
ip link set dev eth0 address 00:00:00:00:00:03
ip link set dev eth0 down
ip link set dev eth0 up
pc3.startup
to eth0 a MAC address is assigned, different from the default one

## Slide 12: a quick look at the lab
ip link set dev eth0 address 00:00:00:00:00:01
ip link set dev eth0 down
ip link set dev eth0 up
pc1.startup
ip link set dev eth0 address 00:00:00:00:00:02
ip link set dev eth0 down
ip link set dev eth0 up
pc2.startup
ip link set dev eth0 address 00:00:00:00:00:03
ip link set dev eth0 down
ip link set dev eth0 up
pc3.startup
the eth0 interface is set down and then up to force the stateless auto-configuration to rely on the new MAC address

## Slide 13: a quick look at the lab
ip link set dev eth0 address 00:00:00:00:00:01
ip link set dev eth0 down
ip link set dev eth0 up
pc1.startup
ip link set dev eth0 address 00:00:00:00:00:02
ip link set dev eth0 down
ip link set dev eth0 up
pc2.startup
ip link set dev eth0 address 00:00:00:00:00:03
ip link set dev eth0 down
ip link set dev eth0 up
pc3.startup
no command is given to configure an IPv6 address or a default gateway, since they are obtained from the stateless auto-configuration

## Slide 14: a quick look at the lab
ip link set dev eth0 address 00:00:00:00:00:a1
ip link set dev eth1 address 00:00:00:00:00:b1
ip link set dev eth0 down
ip link set dev eth0 up
ip link set dev eth1 down
ip link set dev eth1 up
ip address add 2001:0:0:1::1/64 dev eth0
ip address add 2001:0:0:2::1/64 dev eth1
ip route add 2001:0:0:3::/64 via fe80::200:ff:fe00:b2 dev eth1
chmod o-rw /etc/radvd.conf
systemctl start radvd
r1.startup

## Slide 15: a quick look at the lab
ip link set dev eth0 address 00:00:00:00:00:a1
ip link set dev eth1 address 00:00:00:00:00:b1
ip link set dev eth0 down
ip link set dev eth0 up
ip link set dev eth1 down
ip link set dev eth1 up
ip address add 2001:0:0:1::1/64 dev eth0
ip address add 2001:0:0:2::1/64 dev eth1
ip route add 2001:0:0:3::/64 via fe80::200:ff:fe00:b2 dev eth1
chmod o-rw /etc/radvd.conf
systemctl start radvd
r1.startup
to eth0 and eth1 a MAC address is assigned different from the default one

## Slide 16: a quick look at the lab
ip link set dev eth0 address 00:00:00:00:00:a1
ip link set dev eth1 address 00:00:00:00:00:b1
ip link set dev eth0 down
ip link set dev eth0 up
ip link set dev eth1 down
ip link set dev eth1 up
ip address add 2001:0:0:1::1/64 dev eth0
ip address add 2001:0:0:2::1/64 dev eth1
ip route add 2001:0:0:3::/64 via fe80::200:ff:fe00:b2 dev eth1
chmod o-rw /etc/radvd.conf
systemctl start radvd
r1.startup
the eth0 and eth1 interfaces are set down and then up to force the stateless auto-configuration to rely on the new MAC addresses

## Slide 17: a quick look at the lab
ip link set dev eth0 address 00:00:00:00:00:a1
ip link set dev eth1 address 00:00:00:00:00:b1
ip link set dev eth0 down
ip link set dev eth0 up
ip link set dev eth1 down
ip link set dev eth1 up
ip address add 2001:0:0:1::1/64 dev eth0
ip address add 2001:0:0:2::1/64 dev eth1
ip route add 2001:0:0:3::/64 via fe80::200:ff:fe00:b2 dev eth1
chmod o-rw /etc/radvd.conf
systemctl start radvd
r1.startup
a static IPv6 address is given to eth0 and to eth1
consequently, the corresponding LANs are considered directly connected

## Slide 18: a quick look at the lab
ip link set dev eth0 address 00:00:00:00:00:a1
ip link set dev eth1 address 00:00:00:00:00:b1
ip link set dev eth0 down
ip link set dev eth0 up
ip link set dev eth1 down
ip link set dev eth1 up
ip address add 2001:0:0:1::1/64 dev eth0
ip address add 2001:0:0:2::1/64 dev eth1
ip route add 2001:0:0:3::/64 via fe80::200:ff:fe00:b2 dev eth1
chmod o-rw /etc/radvd.conf
systemctl start radvd
r1.startup
the routing table is set;
a row is added to the routing table on how to reach a LAN that is not directly connected; the nexthop is a link-local address

## Slide 19: a quick look at the lab
ip link set dev eth0 address 00:00:00:00:00:a1
ip link set dev eth1 address 00:00:00:00:00:b1
ip link set dev eth0 down
ip link set dev eth0 up
ip link set dev eth1 down
ip link set dev eth1 up
ip address add 2001:0:0:1::1/64 dev eth0
ip address add 2001:0:0:2::1/64 dev eth1
ip route add 2001:0:0:3::/64 via fe80::200:ff:fe00:b2 dev eth1
chmod o-rw /etc/radvd.conf
systemctl start radvd
r1.startup
the correct privileges for radvd.conf are set
and the radvd service is started

## Slide 20: a quick look at the lab
interface eth0
{
AdvSendAdvert on;
MinRtrAdvInterval 3;
MaxRtrAdvInterval 9;
AdvDefaultLifetime 27;
prefix 2001:0:0:1::/64 {};
};
radvd.conf
this configuration file, of the radvd daemon, is in the /etc directory of r1

## Slide 21: router advertisement
radvd is a daemon
it is used to send router advertisement messages
the configuration of radvd is specified in the radvd.conf file

## Slide 22: a quick look at the lab
interface eth0
{
AdvSendAdvert on;
MinRtrAdvInterval 3;
MaxRtrAdvInterval 9;
AdvDefaultLifetime 27;
prefix 2001:0:0:1::/64 {};
};
radvd.conf
interface of the router where the advertisements are sent

## Slide 23: a quick look at the lab
interface eth0
{
AdvSendAdvert on;
MinRtrAdvInterval 3;
MaxRtrAdvInterval 9;
AdvDefaultLifetime 27;
prefix 2001:0:0:1::/64 {};
};
radvd.conf
the announced prefix

## Slide 24: a quick look at the lab
interface eth0
{
AdvSendAdvert on;
MinRtrAdvInterval 3;
MaxRtrAdvInterval 9;
AdvDefaultLifetime 27;
prefix 2001:0:0:1::/64 {};
};
radvd.conf
advertisements are sent
minimum interval between consecutive advertisements
maximum interval between consecutive advertisements
time interval for default gateway validity

## Slide 25: a quick look at the lab
ip link set dev eth0 address 00:00:00:00:00:a1
ip link set dev eth1 address 00:00:00:00:00:b1
ip link set dev eth0 down
ip link set dev eth0 up
ip link set dev eth1 down
ip link set dev eth1 up
ip address add 2001:0:0:1::1/64 dev eth0
ip address add 2001:0:0:2::1/64 dev eth1
ip route add 2001:0:0:3::/64 via fe80::200:ff:fe00:b2 dev eth1
chmod o-rw /etc/radvd.conf
systemctl start radvd
r1.startup
similar configuration for router r2

## Slide 26: start the lab
start the lab
user@localhost:~$ cd kathara-lab_basic-ipv6
user@localhost:~/kathara-lab_basic-ipv6$ lstart

## Slide 27: useful commands

## Slide 28: check the IPv6 addresses
on r1, and r2
  perform the ip address command, to check the addresses assigned to the interfaces
    the ip -6 address command shows only the IPv6 addresses
    look at eth and loopback interfaces

## Slide 29: check the IPv6 addresses
root@r1:/# ip address
1: lo: <LOOPBACK,UP,LOWER_UP> mtu 65536 qdisc noqueue state UNKNOWN group default qlen 1000
link/loopback 00:00:00:00:00:00 brd 00:00:00:00:00:00
inet 127.0.0.1/8 scope host lo
valid_lft forever preferred_lft forever
inet6 ::1/128 scope host
valid_lft forever preferred_lft forever
11: eth0: <BROADCAST,MULTICAST,UP,LOWER_UP> mtu 1500 qdisc fq_codel state UP group default qlen 1000
link/ether 00:00:00:00:00:a1 brd ff:ff:ff:ff:ff:ff
inet6 2001:0:0:1::1/64 scope global
valid_lft forever preferred_lft forever
inet6 fe80::200:ff:fe00:a1/64 scope link
valid_lft forever preferred_lft forever
12: eth1: <BROADCAST,MULTICAST,UP,LOWER_UP> mtu 1500 qdisc fq_codel state UP group default qlen 1000
link/ether 00:00:00:00:00:b1 brd ff:ff:ff:ff:ff:ff
inet6 2001:0:0:2::1/64 scope global
valid_lft forever preferred_lft forever
inet6 fe80::200:ff:fe00:b1/64 scope link
valid_lft forever preferred_lft forever
r1
eth0
global unicast: 2001:0:0:1::1/64
link-local: fe80::200:ff:fe00:a1/64
eth1
global unicast: 2001:0:0:2::1/64
link-local: fe80::200:ff:fe00:b1/64
loopback
IPv4: 127.0.0.1/8
IPv6: ::1/128

## Slide 30: check the router routing table
on r1 and r2
  perform the routel -6 command, to check the routing table

## Slide 31: check the router routing table
root@r1:/# routel -6
Dst Gateway Prefsrc Protocol Scope Dev Table
::1 kernel lo
2001:0:0:1:: kernel eth0
2001:0:0:1::1 kernel eth0
2001:0:0:1::/64 kernel eth0
2001:0:0:2:: kernel eth1
2001:0:0:2::1 kernel eth1
2001:0:0:2::/64 kernel eth1
2001:0:0:3::/64 fe80::200:ff:fe00:b2 eth1
fe80:: kernel eth0
fe80:: kernel eth1
fe80::200:ff:fe00:a1 kernel eth0
fe80::200:ff:fe00:b1 kernel eth1
fe80::/64 kernel eth0
fe80::/64 kernel eth1
ff00::/8 kernel eth0
ff00::/8 kernel eth1
r1
Lan B
Lan A
Lan C
R2 link local address on B
link-local addresses on A and B
general multicast prefix

## Slide 32: check auto-configured IPv6 addresses
on pc1, pc2, pc3
  perform the ip address command, to check the IPv6 addresses assigned to the interfaces by the stateless auto-configuration
    possibly, perform the ip -6 address command
    look at eth and loopback interfaces

## Slide 33: check auto-configured IPv6 addresses
root@pc1:/# ip address
1: lo: <LOOPBACK,UP,LOWER_UP> mtu 65536 qdisc noqueue state UNKNOWN group default qlen 1000
link/loopback 00:00:00:00:00:00 brd 00:00:00:00:00:00
inet 127.0.0.1/8 scope host lo
valid_lft forever preferred_lft forever
inet6 ::1/128 scope host
valid_lft forever preferred_lft forever
7: eth0: <BROADCAST,MULTICAST,UP,LOWER_UP> mtu 1500 qdisc fq_codel state UP group default qlen 1000
link/ether 00:00:00:00:00:01 brd ff:ff:ff:ff:ff:ff
inet6 2001::1:200:ff:fe00:1/64 scope global dynamic mngtmpaddr
valid_lft 86394sec preferred_lft 14394sec
inet6 fe80::200:ff:fe00:1/64 scope link
valid_lft forever preferred_lft forever
pc1
loopback
IPv4: 127.0.0.1/8
IPv6: ::1/128
eth0
global unicast: 2001::1:200:ff:fe00:1/64
link-local: fe80::200:ff:fe00:1/64

## Slide 34: check the default route
on pc1, pc2, and pc3
  perform the routel -6 command, to check the presence of a default route

## Slide 35: check the default route
on pc1, pc2, and pc3
  perform the routel -6 command, to check the presence of a default route
root@pc1:/# routel -6
Dst Gateway Prefsrc Protocol Scope Dev
::1 kernel lo
2001:0:0:1:: kernel eth0
2001::1:200:ff:fe00:1 kernel eth0
2001:0:0:1::/64 kernel eth0
fe80:: kernel eth0
fe80::200:ff:fe00:1 kernel eth0
fe80::/64 kernel eth0
ff00::/8 kernel eth0
default fe80::200:ff:fe00:a1 ra eth0
r1
default route by r1
loopback prefix
learned by a router advertisment
link-local address of r1 on A

## Slide 36: sniff the traffic
connect the wireshark device to collision domain C
open any browser on the host machine
  on localhost:3000
  sniff eth1
user@localhost:~/kathara-lab_basic-ipv6$ kathara lconfig -n wireshark --add C

## Slide 37: ping from pc3 to pc2 and related ICMPv6 behaviour

## Slide 38: on pc3
inspect the neighbor cache
execute a ping command towards pc2
inspect again the neighbor cache
give a look at the packets captured by Wireshark

## Slide 39: inspecting the neighbor cache
similar to the IPv4 ARP cache
root@pc3:/# ip neigh
fe80::200:ff:fe00:c1 dev eth0 lladdr 00:00:00:00:00:c1 router STALE
fe80::200:ff:fe00:2 dev eth0 lladdr 00:00:00:00:00:02 STALE
pc3
link-local address of r2 on C
link-local address of pc2

## Slide 40: ping and inspect the neighbor cache
root@pc3:/# ping 2001::3:200:ff:fe00:2
PING 2001::3:200:ff:fe00:2(2001::3:200:ff:fe00:2) 56 data bytes
64 bytes from 2001::3:200:ff:fe00:2: icmp_seq=1 ttl=64 time=1.50 ms
64 bytes from 2001::3:200:ff:fe00:2: icmp_seq=2 ttl=64 time=0.585 ms
64 bytes from 2001::3:200:ff:fe00:2: icmp_seq=3 ttl=64 time=0.775 ms
^C
--- 2001::3:200:ff:fe00:2 ping statistics ---
3 packets transmitted, 3 received, 0% packet loss, time 2040ms
rtt min/avg/max/mdev = 0.585/0.953/1.500/0.394 ms
root@pc3:/# ip neigh
2001::3:200:ff:fe00:2 dev eth0 lladdr 00:00:00:00:00:02 router REACHABLE
fe80::200:ff:fe00:c1 dev eth0 lladdr 00:00:00:00:00:c1 router STALE
fe80::200:ff:fe00:2 dev eth0 lladdr 00:00:00:00:00:02 DELAY
pc3
global IPv6 address of pc2

## Slide 41: inspecting the neighbor cache
traffic within the same network does not traverse routers
r1
r2
C
pc1
pc2
eth0
eth0
200.1.1.0/24
.7
.1
pc3
eth0
.3

## Slide 42: inspecting the neighbor cache
communications are usually bi-directional
the receiver of the neighbor solicitation learns the mac address of the other party
root@pc2:/# ip neigh
fe80::200:ff:fe00:3 dev eth0 lladdr 00:00:00:00:00:03 router STALE
2001::3:200:ff:fe00:3 dev eth0 lladdr 00:00:00:00:00:03 router STALE
fe80::200:ff:fe00:c1 dev eth0 lladdr 00:00:00:00:00:c1 router STALE
pc2
global IPv6 address of pc3

## Slide 43: wireshark
periodic router advertisments

## Slide 44: wireshark
neighbor solicitation

## Slide 45: wireshark
neighbor solicitation
neighbor advertisment

## Slide 46: wireshark
neighbor solicitation
neighbor advertisment
At the end of the ping a unicast neighbor solicitation/advertisment dialogue takes place

## Slide 47: ping from pc2 to pc1 and related ICMPv6 behavior

## Slide 48: sniff the traffic
connect the wireshark host to collision domain B
open any browser on the host machine
  on localhost:3000
  sniff eth2
user@localhost:~/kathara-lab_basic-ipv6$ kathara lconfig -n wireshark --add B

## Slide 49: on pc2
execute a ping command towards pc1
root@pc2:/# ping 2001::1:200:ff:fe00:1
PING 2001::1:200:ff:fe00:1(2001::1:200:ff:fe00:1) 56 data bytes
64 bytes from 2001::1:200:ff:fe00:1: icmp_seq=1 ttl=62 time=2.58 ms
64 bytes from 2001::1:200:ff:fe00:1: icmp_seq=2 ttl=62 time=1.52 ms
--- 2001::1:200:ff:fe00:1 ping statistics ---
2 packets transmitted, 2 received, 0% packet loss, time 3011ms
rtt min/avg/max/mdev = 1.267/1.880/2.575/0.515 ms
pc2

## Slide 50: inspecting the neighbor cache
A
r1
r2
C
B
pc1
pc2
eth0
eth0
eth0
eth1
eth1
eth0
2001:0:0:1::/64
2001:0:0:3::/64
2001:0:0:2::/64
.1
.1
.1
.2
pc3
eth0
0:1
0:2
0:3
0:a1
0:c1
0:b1
0:b2

## Slide 51: inspecting the neighbor cache
when IP traffic is addressed outside the local network, the sender needs the mac address of the router
ICMPv6 ND requests can get replies only within the local network
root@pc2:/# ip neigh
fe80::200:ff:fe00:c1 dev eth0 lladdr 00:00:00:00:00:c1 router STALE
fe80::200:ff:fe00:3 dev eth0 lladdr 00:00:00:00:00:03 STALE
pc2
mac address of eth0 on r2

## Slide 52: inspecting the neighbor cache
root@r1:/# ip neigh
fe80::200:ff:fe00:b2 dev eth1 lladdr 00:00:00:00:00:b2 router STALE
fe80::200:ff:fe00:1 dev eth0 lladdr 00:00:00:00:00:01 router STALE
2001::1:200:ff:fe00:1 dev eth0 lladdr 00:00:00:00:00:01 router STALE
fe80::200:ff:fe00:a1 dev eth0 lladdr 00:00:00:00:00:a1 router STALE
r1
what about routers?
routers perform ND too (hence have neighbor caches)
pc1
r2 (eth1)
root@r2:/# ip neigh
fe80::200:ff:fe00:c1 dev eth0 lladdr 00:00:00:00:00:c1 router STALE
fe80::200:ff:fe00:3 dev eth0 lladdr 00:00:00:00:00:03 router STALE
fe80::200:ff:fe00:b1 dev eth1 lladdr 00:00:00:00:00:b1 router STALE
2001::3:200:ff:fe00:2 dev eth0 lladdr 00:00:00:00:00:02 router STALE
fe80::200:ff:fe00:2 dev eth0 lladdr 00:00:00:00:00:02 router STALE
r2
pc2
r1 (eth1)
pc1
pc2

## Slide 53: wireshark
which is the mac address of r1

## Slide 54: understanding the whole picture
r1
r2
pc1
pc2
ICMP NA
ICMP NS
ICMP NA
ICMP NS
ICMP NA
ICMP NS
icmp echo req
icmp echo req
icmp echo req
icmp echo reply
icmp echo reply
icmp echo reply
time
A
B
C

## Slide 55: traceroute from pc2 to pc1 and related ICMPv6 behaviour

## Slide 56: sniff the traffic
the wireshark host is already connected to collision domain C
open any browser on the host machine
  on localhost:3000
  sniff eth1

## Slide 57: on pc2
execute a traceroute command towards pc1
root@pc2:/# traceroute 2001::1:200:ff:fe00:1 -z 1
traceroute to 2001::1:200:ff:fe00:1 (2001::1:200:ff:fe00:1), 30 hops max, 80 byte packets
1 2001:0:0:3::1 (2001:0:0:3::1) 0.442 ms 0.580 ms 0.602 ms
2 2001:0:0:2::1 (2001:0:0:2::1) 0.878 ms 1.175 ms 0.751 ms
3 2001::1:200:ff:fe00:1 (2001::1:200:ff:fe00:1) 1.078 ms 1.434 ms 1.708 ms
root@pc2:/#
pc2
eth0 of r2
eth1 of r1
eth0 of pc1
Minimal time (sec. if ≤10, ms if >10) interval between probes (default 0)

## Slide 58: wireshark
Time to live: 1
udp packet and corresponding ICMP Time-to-live exceeded

## Slide 59: proposed exercises
check the different error messages obtained by trying to ping an unreachable destination in the case of
  local destination
  non-local destination
which packets are exchanged in the local collision domain in the two cases?